## Slide 1: Digital Design
Chapter 5:
Register-Transfer Level
(RTL) Design
Slides to accompany the textbook Digital Design, First Edition,
by Frank Vahid, John Wiley and Sons Publishers, 2007.
http://www.ddvahid.com
Copyright © 2007 Frank Vahid
Instructors of courses requiring Vahid's Digital Design textbook (published by John Wiley and Sons) have permission to modify and use these slides for customary course-related activities, subject to keeping this copyright notice in place and unmodified. These slides may be posted as unanimated pdf versions on publicly-accessible course websites.. PowerPoint source (or pdf with animations) may not be posted to publicly-accessible websites, but may be posted for students on internal protected sites or distributed directly to students by other electronic means. Instructors may make printouts of the slides available to students for a reasonable photocopying charge, without incurring royalties. Any other use requires explicit permission. Instructors may obtain PowerPoint source or obtain special use permissions from Wiley – see http://www.ddvahid.com for information.

## Slide 2: Introduction
Chapter 3: Controllers
  Control input/output: single bit (or just a few) representing event or state
  Finite-state machine describes behavior; implemented as state register and combinational logic
Chapter 4: Datapath components
  Data input/output: Multiple bits collectively representing single entity
  Datapath components included registers, adders, ALU, comparators, register files, etc.
This chapter: custom processors
  Processor: Controller and datapath components working together to implement an algorithm
5.1
si
z
e
ansis
Combinational
logic
n0
s1
s0
n1
bo
bi
clk
State register
FSM
inputs
FSM
outputs
ALU
Comparator
Register file
Register
Combinational
logic
n0
s1
s0
n1
bo
bi
State register
Register file
ALU
Datapath
Controller
Note: Slides with animation are denoted with a small red "a" near the animated items

## Slide 3: RTL Design: Capture Behavior, Convert to Circuit
Recall
  Chapter 2: Combinational Logic Design
    First step: Capture behavior (using equation or truth table)
    Remaining steps: Convert to circuit
  Chapter 3: Sequential Logic Design
    First step: Capture behavior (using FSM)
    Remaining steps: Convert to circuit
RTL Design (the method for creating custom processors)
  First step: Capture behavior (using high-level state machine, to be introduced)
  Remaining steps: Convert to circuit
Capture behavior
Convert to circuit

## Slide 4: RTL Design Method
5.2

## Slide 5: RTL Design Method: “Preview” Example
Soda dispenser
  c: bit input, 1 when coin deposited
  a: 8-bit input having value of deposited coin
  s: 8-bit input having cost of a soda
  d: bit output, processor sets to 1 when total value of deposited coins equals or exceeds cost of a soda
a
s
c
d
Soda
dispenser
processor
25
1
0
25
1
1
50
0
0
0
0
tot:
25
tot:
50
How can we precisely describe this processor’s behavior?
a
a
s
c
d
Soda
dispenser
processor

## Slide 6: Preview Example: Step 1 -- Capture High-Level State Machine
Declare local register tot
Init state: Set d=0, tot=0
Wait state: wait for coin
  If see coin, go to Add state
Add state: Update total value: tot = tot + a
  Remember, a is present coin’s value
  Go back to Wait state
In Wait state, if tot >= s, go to Disp(ense) state
Disp state: Set d=1 (dispense soda)
  Return to Init state
Inputs: c (bit), a (8 bits), s (8 bits)
Outputs: d (bit)
Local registers: tot (8 bits)
Wait
Add
Disp
I
nit
d=0
tot=0
c’*(tot<s)
d=1
c
tot=tot+a
8
8
a
s
c
d
Soda
dispenser
processor
c’*(tot<s)’

## Slide 7: Preview Example: Step 2 -- Create Datapath
Need tot register
Need 8-bit comparator to compare s and tot
Need 8-bit adder to perform tot = tot + a
Wire the components as needed for above
Create control input/outputs, give them names
ld
clr
tot
8-bit
<
8-bit
adder
8
8
8
8
s
a
Datapath
tot_ld
tot_clr
tot_lt_s
I
nputs
:
c
(bit),
a(8 bits)
,
s
(8 bits)
O
utputs
:
d (bit)
L
ocal
r
e
g
is
t
ers
:
t
ot (8 bits)
W
ait
A
dd
Disp
I
nit
d=0
t
ot=0
c
‘
(
t
ot<s)
‘
c
‘
*
(
t
ot<s)
d=1
c
t
ot=
t
ot+a

## Slide 8: Preview Example: Step 3 – Connect Datapath to a Controller
Controller’s inputs
  External input c (coin detected)
  Input from datapath comparator’s output, which we named tot_lt_s
Controller’s outputs
  External output d (dispense soda)
  Outputs to datapath to load and clear the tot register
tot_lt_s
tot_clr
tot_ld
Controller
Datapath
s
c
d
a
8
8
ld
clr
t
ot
8-bit
<
8-bit
adder
8
8
8
8
s
a
D
a
tap
a
th
t
ot_ld
t
ot_clr
t
ot_lt_s

## Slide 9: Preview Example: Step 4 – Derive the Controller’s FSM
Same states and arcs as high-level state machine
But set/read datapath control signals for all datapath operations and conditions
tot_lt_s
tot_clr
tot_ld
Controller
Datapath
s
c
d
a
8
8
ld
clr
tpt
8-bit
<
8-bit
adder
8
8
8
8
s
a
Datapath
tot_ld
tot_clr
tot_lt_s
Inputs:
:
c
,
tot_lt_s
(bit)
Outputs:
d
,
tot_ld
,
tot_clr
(bit)
W
ait
Disp
I
nit
d=0
tot_clr=1
c’*
tot_lt_s’
c
’
*
tot_lt_s
d=1
c
tot_ld=1
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add

## Slide 10: Preview Example: Completing the Design
Implement the FSM as a state register and logic
  As in Ch3
  Table shown on right
Inputs:
:
c
,
tot_lt_s
(bit)
Outputs:
d
,
tot_ld
,
tot_clr
(bit)
W
ait
Disp
I
nit
d=0
tot_clr=1
c’*
tot_lt_s’
c
’
*
tot_lt_s
d=1
c
tot_ld=1
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add

## Slide 11: Step 1: Create a High-Level State Machine
Let’s consider each step of the RTL design process in more detail
Step 1
  Soda dispenser example
  Not an FSM because:
    Multi-bit (data) inputs a and s
    Local register tot
    Data operations tot=0, tot<s, tot=tot+a.
  Useful high-level state machine:
    Data types beyond just bits
    Local registers
    Arithmetic equations/expressions
I
nputs
:
c
(bit),
a (8 bits)
,
s (8 bits)
O
utputs
:
d (bit)
L
ocal
r
e
g
is
t
ers
:
t
ot (8 bits)
W
ait
Disp
I
nit
d=0
t
ot=0
c’
(
t
ot<s
)
d=1
c
t
ot=
t
ot+a
c’
(
t
ot<s
)’

## Slide 12: Step 1 Example: Laser-Based Distance Measurer
Example of how to create a high-level state machine to describe desired processor behavior
Laser-based distance measurement – pulse laser, measure time T to sense reflection
  Laser light travels at speed of light, 3*108 m/sec
  Distance is thus D = T sec * 3*108 m/sec / 2
Object of
interest
D
2D = T sec * 3*108 m/sec
sensor
laser
T (in seconds)

## Slide 13: Step 1 Example: Laser-Based Distance Measurer
Inputs/outputs
  B: bit input, from button to begin measurement
  L: bit output, activates laser
  S: bit input, senses laser reflection
  D: 16-bit output, displays computed distance
sensor
laser
T (in seconds)
Laser-based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor

## Slide 14: Step 1 Example: Laser-Based Distance Measurer
Step 1: Create high-level state machine
Begin by declaring inputs and outputs
Create initial state, name it S0
  Initialize laser to off (L=0)
  Initialize displayed distance to 0 (D=0)
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor
Inputs:
B
, S
(1 bit each)
Outputs:
L (bit), D (16 bits)
S0
?
L = 0 (laser off)
D = 0 (distance = 0)
a

## Slide 15: Step 1 Example: Laser-Based Distance Measurer
Add another state, call S1, that waits for a button press
  B’ – stay in S1, keep waiting
  B – go to a new state S2
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)
S0
L = 0
D = 0
S1
?
B’ (button not pressed)
B
(button
pressed)
S0
Q: What should S2 do?
A: Turn on the laser
a
a
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor

## Slide 16: Step 1 Example: Laser-Based Distance Measurer
Add a state S2 that turns on the laser (L=1)
Then turn off laser (L=0) in a state S3
S0
S1
S2
L = 0
D = 0
L = 1
(laser on)
S3
L = 0
(laser off)
B’
B
a
Q: What do next?
A: Start timer, wait to sense reflection
a
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)

## Slide 17: Step 1 Example: Laser-Based Distance Measurer
Stay in S3 until sense reflection (S)
To measure time, count cycles for which we are in S3
  To count, declare local register Dctr
  Increment Dctr each cycle in S3
  Initialize Dctr to 0 in S1. S2 would have been O.K. too
Lase
r
-based
distan
c
e
measu
r
er
16
f
r
om but
t
on
t
o displ
a
y
S
L
D
B
t
o laser
f
r
om sensor
Local Registers: Dctr (16 bits)
S0
S1
S2
S3
L = 0
D = 0
L = 1
L = 0
Dctr = Dctr + 1
(count cycles)
Dctr = 0
(reset cycle
count)
B’
B
S’ (no reflection)
S (reflection)
?
a
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)

## Slide 18: Step 1 Example: Laser-Based Distance Measurer
Once reflection detected (S), go to new state S4
  Calculate distance
  Assuming clock frequency is 3x108, Dctr holds number of meters, so D=Dctr/2
After S4, go back to S1 to wait for button again
Lase
r
-based
distan
c
e
measu
r
er
16
f
r
om but
t
on
t
o displ
a
y
S
L
D
B
t
o laser
f
r
om sensor
S0
S1
S2
S3
L = 0
D = 0
L = 1
L=0
Dctr = Dctr + 1
Dctr = 0
B’
S’
B
S
D = Dctr / 2
(calculate D)
S4
a
Local Registers: Dctr (16 bits)
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)

## Slide 19: Step 2: Create a Datapath
Datapath must
  Implement data storage
  Implement data computations
Look at high-level state machine, do three substeps
  (a) Make data inputs/outputs be datapath inputs/outputs
  (b) Instantiate declared registers into the datapath (also instantiate a register for each data output)
  (c) Examine every state and transition, and instantiate datapath components and connections to implement any data computations
Instantiate: to introduce a new component into a design.

## Slide 20: Step 2 Example: Laser-Based Distance Measurer
(a) Make data inputs/outputs be datapath inputs/outputs
(b) Instantiate declared registers into the datapath (also instantiate a register for each data output)
(c) Examine every state and transition, and instantiate datapath components and connections to implement any data computations
D
a
tap
a
th
D
r
eg_clr
D
c
tr_clr
D
c
tr_c
n
t
D
r
eg_ld
Local Registers: Dctr (16 bits)
S0
S1
S2
S3
L = 0
D = 0
L = 1
L=0
Dctr = Dctr + 1
Dctr = 0
B
‘
S
‘
B
S
D = Dctr / 2
(calculate D)
S4
load
Q
I
D
r
eg: 16-bit
r
e
g
is
t
er
Q
D
c
t
r
: 16-bit
u
p
-
c
ou
n
t
er
16
D
clear
clear
c
ou
n
t
a
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)

## Slide 21: Step 2 Example: Laser-Based Distance Measurer
(c) (continued) Examine every state and transition, and instantiate datapath components and connections to implement any data computations
clear
c
ou
n
t
clear
load
Q
Q
I
D
c
t
r
: 16-bit
u
p
-
c
ou
n
t
er
D
r
eg: 16-bit
r
e
g
is
t
er
16
D
D
a
tap
a
th
D
r
eg_clr
D
c
tr_clr
D
c
tr_c
n
t
D
r
eg_ld
16
16
>>1
a
Local Registers: Dctr (16 bits)
S0
S1
S2
S3
L = 0
D = 0
L = 1
L=0
Dctr = Dctr + 1
Dctr = 0
B
‘
S
‘
B
S
D = Dctr / 2
(calculate D)
S4
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)

## Slide 22: Step 2 Example Showing Mux Use
Introduce mux when one component input can come from more than one source
T0
T1
R = E + F
R = R + G
E
,
F
, G, R (16 bits)
L
ocal
r
e
g
is
t
ers
:
(
a
)
E
F
G
A
B
+
R
add_A_s0
add_B_s0
2
×
1
2
×
1
(
d
)
×
×
a
E
F
G
A
B
+
R
(
b
)
E
F
G
A
B
+
R
(
c
)

## Slide 23: Step 3: Connecting the Datapath to a Controller
Laser-based distance measurer example
Easy – just connect all control signals between controller and datapath
300 M
H
z Clock
D
B
L
S
16
to display
from button
Controller
to laser
from sensor
Datapath
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_cnt
clear
c
ou
n
t
clear
load
Q
Q
I
D
c
t
r
: 16-bit
u
p
-
c
ou
n
t
er
D
r
eg: 16-bit
r
e
g
is
t
er
16
D
D
a
tap
a
th
D
r
eg_clr
D
c
tr_clr
D
c
tr_c
n
t
D
r
eg_ld
16
16
>>1

## Slide 24: Step 4: Deriving the Controller’s FSM
FSM has same structure as high-level state machine
  Inputs/outputs all bits now
  Replace data operations by bit operations using datapath
300 M
H
z Clock
D
B
L
S
16
t
o displ
a
y
f
r
om but
t
on
C
o
n
t
r
oller
t
o laser
f
r
om sensor
D
a
tap
a
th
D
r
eg_clr
D
r
eg_ld
D
c
tr_clr
D
c
tr_c
n
t
Inputs: B, S
Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
S0
S1
S2
S3
L = 0
L = 1
L = 0
L = 0
B’
S’
B
S
S4
L = 0
Inputs: B, S (1 bit each)
Outputs: L (bit), D (16 bits)
Local Registers: Dctr (16 bits)
S0
S1
S2
S3
L = 0
D = 0
L = 1
L=0
Dctr = Dctr + 1
Dctr = 0
B’
S’
B
S
D = Dctr / 2
(calculate D)
S4
a
Dreg_clr = 1
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 0
(laser off)
(clear D reg)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 1
Dctr_cnt = 0
(clear count)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 0
(laser on)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 1
(laser off)
(count up)
Dreg_clr = 0
Dreg_ld = 1
Dctr_clr = 0
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)

## Slide 25: Step 4: Deriving the Controller’s FSM
Using shorthand of outputs not assigned implicitly assigned 0
a
S0
S1
S2
S3
L = 0
L = 1
L = 0
L = 0
B’
S’
B
S
S4
L = 0
Dreg_clr = 1
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 0
(laser off)
(clear D reg)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 1
Dctr_cnt = 0
(clear count)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 0
(laser on)
Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 1
(laser off)
(count up)
Dreg_clr = 0
Dreg_ld = 1
Dctr_clr = 0
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)
S0
S1
S2
S3
L = 0
L = 1
L = 0
B’
S’
B
S
(laser on)
S4
Inputs: B, S
Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
Dreg_clr = 1
(laser off)
(clear D reg)
Dctr_clr = 1
(clear count)
Dctr_cnt = 1
(laser off)
(count up)
Dreg_ld = 1
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)

## Slide 26: Step 4
Implement FSM as state register and logic (Ch3) to complete the design
300 MHz Clock
D
B
L
S
16
to display
from button
Controller
to laser
from sensor
Datapath
Dreg_clr
S0
S1
S2
S3
L = 0
L = 1
L = 0
B’
S’
B
S
(laser on)
S4
Inputs: B, S
Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
Dreg_clr = 1
(laser off)
(clear D reg)
Dctr_clr = 1
(clear count)
Dctr_cnt = 1
(laser off)
(count up)
Dreg_ld = 1
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)
Dreg_ld
Dctr_clr
Dctr_cnt
clear
c
ou
n
t
clear
load
Q
Q
I
D
c
t
r
: 16-bit
u
p
-
c
ou
n
t
er
D
r
eg: 16-bit
r
e
g
is
t
er
16
D
D
a
tap
a
th
D
r
eg_clr
D
c
tr_clr
D
c
tr_c
n
t
D
r
eg_ld
16
16
>>1

## Slide 27: RTL Design Examples and Issues
We’ll use several more examples to illustrate RTL design
Example: Bus interface
  Master processor can read register from any peripheral
    Each register has unique 4-bit address
    Assume 1 register/periph.
  Sets rd=1, A=address
  Appropriate peripheral places register data on 32-bit D lines
    Periph’s address provided on Faddr inputs (maybe from DIP switches, or another register)
5.3
32
4
A
r
d
D
Per0
Per1
Per15
Master
processor
Faddr
4
A
D
r
d
Bus interface
Main part
Peripheral
Q
32
to/from processor bus
32
4

## Slide 28: RTL Example: Bus Interface
Step 1: Create high-level state machine
  State WaitMyAddress
    Output “nothing” (“Z”) on D, store peripheral’s register value Q into local register Q1
    Wait until this peripheral’s address is seen (A=Faddr) and rd=1
  State SendData
    Output Q1 onto D, wait for rd=0 (meaning main processor is done reading the D lines)
WaitMyAddress
Inputs: rd (bit); Q (32 bits); A, Faddr (4 bits)
Outputs: D (32 bits)
Local register: Q1 (32 bits)
rd’
rd
SendData
D = “Z”
Q1 = Q
(A = Faddr)
and rd
((A = Faddr)
and rd’)
D = Q1

## Slide 29: RTL Example: Bus Interface
WaitMyAddress
Inputs: rd (bit); Q (32 bits); A, Faddr (4 bits)
Outputs: D (32 bits)
Local register: Q1 (32 bits)
rd’
rd
SendData
D = “Z”
Q1 = Q
(A = Faddr)
and rd
((A = Faddr)
and rd’)
D = Q1

## Slide 30: RTL Example: Bus Interface
WaitMyAddress
Inputs: rd (bit); Q (32 bits); A, Faddr (4 bits)
Outputs: D (32 bits)
Local register: Q1 (32 bits)
rd’
rd
SendData
D = “Z”
Q1 = Q
(A = Faddr)
and rd
((A = Faddr)
and rd)’
D = Q1
Step 2: Create a datapath
  (a) Datapath inputs/outputs
  (b) Instantiate declared registers
  (c) Instantiate datapath components and connections
Datapath
Bus interface
Q1_ld
ld
Q1
F
Q
addr
4
4
32
A
D_en
A_eq_
F
addr
= (4-bit)
32
32
D
a

## Slide 31: RTL Example: Bus Interface
Step 3: Connect datapath to controller
Step 4: Derive controller’s FSM
a
WaitMyAddress
Inputs: rd (bit); Q (32 bits); A, Faddr (4 bits)
Outputs: D (32 bits)
Local register: Q1 (32 bits)
rd’
rd
SendData
D = “Z”
Q1 = Q
(A = Faddr)
and rd
((A = Faddr)
and rd)’
D = Q1
rd
Inputs: rd, A_eq_Faddr (bit)
Outputs: Q1_ld, D_en (bit)
W
ait
M
y
A
dd
r
ess
r
d
‘
r
d
S
endD
a
ta
D_en = 0
Q1_ld = 1
D_en = 1
Q1_ld = 0
A_eq_
F
addr
and
r
d
(
A_eq_
F
addr
and
r
d)
‘
Datapath
Bus interface
Q1_ld
ld
Q1
Faddr
Q
4
4
32
A
D_en
A_eq_Faddr
= (4-bit)
32
32
D

## Slide 32: RTL Example: Video Compression – Sum of Absolute Differences
Video is a series of frames (e.g., 30 per second)
Most frames similar to previous frame
  Compression idea: just send difference from previous frame
Digitized
frame 2
1 Mbyte
Frame 2
Digitized
frame 1
Frame 1
1 Mbyte
(
a
)
Digitized
frame 1
Frame 1
1 Mbyte
(
b
)
Only difference: ball moving
a
Difference of
2 from 1
0.01 Mbyte
Frame 2
Just send difference

## Slide 33: RTL Example: Video Compression – Sum of Absolute Differences
Need to quickly determine whether two frames are similar enough to just send difference for second frame
  Compare corresponding 16x16 “blocks”
    Treat 16x16 block as 256-byte array
  Compute the absolute value of the difference of each array item
  Sum those differences – if above a threshold, send complete frame for second frame; if below, can use difference method (using another technique, not described)
Frame 2
Frame 1
compare
Each is a pixel, assume represented as 1 byte
(actually, a color picture might have 3 bytes per pixel, for intensity of red, green, and blue components of pixel)

## Slide 34: RTL Example: Video Compression – Sum of Absolute Differences
Want fast sum-of-absolute-differences (SAD) component
  When go=1, sums the differences of element pairs in arrays A and B, outputs that sum
B
A
go
SAD
sad
256-byte array
256-byte array
integer

## Slide 35: RTL Example: Video Compression – Sum of Absolute Differences
S0: wait for go
S1: initialize sum and index
S2: check if done (i>=256)
S3: add difference to sum, increment index
S4: done, write to output sad_reg
B
A
go
SAD
sad
Inputs: A, B (256 byte memory); go (bit)
Outputs: sad (32 bits)
Local registers: sum, sad_reg (32 bits); i (9 bits)
!go
S0
go
S1
sum = 0
i = 0
S3
sum=sum+abs(A[i]-B[i])
i=i+1
S4
sad_
r
eg = sum
S2
i<256
(i<256)’
a

## Slide 36: RTL Example: Video Compression – Sum of Absolute Differences
Step 2: Create datapath
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sad_reg_ld
Datapath
sum
sad_reg
sad
AB_addr
A_data
B_data
<256
9
32
8
8
8
8
32
32
32
i
–
+
abs
Inputs: A, B (256 byte memory); go (bit)
Outputs: sad (32 bits)
Local registers: sum, sad_reg (32 bits); i (9 bits)
!go
S0
go
S1
sum = 0
i = 0
S3
sum=sum+abs(A[i]-B[i])
i=i+1
S4
sad_
reg=sum
S2
i<256
(i<256)’
a

## Slide 37: RTL Example: Video Compression – Sum of Absolute Differences
Step 3: Connect to controller
Step 4: Replace high-level state machine by FSM
S0
S1
S2
S3
S4
go’
go
go
AB_
r
d
sum=0
i=0
i<256
sum=sum+abs(A[i]-B[i])
i=i+1
sad_reg=sum
Controller
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sad_reg_ld
sum
sad_reg
sad
AB_addr
A_data
B_data
<256
9
32
8
8
8
8
32
32
32
i
–
+
abs
a
sum_ld=1; AB_rd=1
sad_reg_ld=1
i_inc=1
i_lt_256
i_clr=1
sum_clr=1
i_lt_256’

## Slide 38: RTL Example: Video Compression – Sum of Absolute Differences
Comparing software and custom circuit SAD
  Circuit: Two states (S2 & S3) for each i, 256 i’s 512 clock cycles
  Software: Loop (for i = 1 to 256), but for each i, must move memory to local registers, subtract, compute absolute value, add to sum, increment i – say about 6 cycles per array item  256*6 = 1536 cycles
  Circuit is about 3 times (300%) faster
  Later, we’ll see how to build SAD circuit that is even faster
S3
sum=sum+abs(A[i]-B[i])
i=i+1
S2
i<256
(i<256)’

## Slide 39: RTL Design Pitfalls and Good Practice
Common pitfall: Assuming register is update in the state it’s written
  Final value of Q?
  Final state?
  Answers may surprise you
    Value of Q unknown
    Final state is C, not D
  Why?
    State A: R=99 and Q=R happen simultaneously
    State B: R not updated with R+1 until next clock cycle, simultaneously with state register being updated

## Slide 40: RTL Design Pitfalls and Good Practice
Solutions
  Read register in following state (Q=R)
  Insert extra state so that conditions use updated value
  Other solutions are possible, depends on the example

## Slide 41: RTL Design Pitfalls and Good Practice
Common pitfall: Reading outputs
  Outputs can only be written
  Solution: Introduce additional register, which can be written and read
T
S
P=P+B
P=A
(
a
)
Inputs: A, B (8 bits)
Outputs: P (8 bits)
Inputs: A, B (8 bits)
Outputs: P (8 bits)
Local register: R (8 bits)
T
S
P=R+B
R=A
P=A
(
b
)

## Slide 42: RTL Design Pitfalls and Good Practice
Good practice: Register all data outputs
  In fig (a), output P would show spurious values as addition computes
    Furthermore, longest register-to-register path, which determines clock period, is not known until that output is connected to another component
  In fig (b), spurious outputs reduced, and longest register-to-register path is clear
+
R
B
P
(a)
+
R
Preg
B
P
(b)

## Slide 43: Control vs. Data Dominated RTL Design
Designs often categorized as control-dominated or data-dominated
  Control-dominated design – Controller contains most of the complexity
  Data-dominated design – Datapath contains most of the complexity
  General, descriptive terms – no hard rule that separates the two types of designs
  Laser-based distance measurer – control dominated
  Bus interface, SAD circuit – mix of control and data
  Now let’s do a data dominated design

## Slide 44: Data Dominated RTL Design Example: FIR Filter
Filter concept
  Suppose X is data from a temperature sensor, and particular input sequence is 180, 180, 181, 240, 180, 181 (one per clock cycle)
  That 240 is probably wrong!
    Could be electrical noise
  Filter should remove such noise in its output Y
  Simple filter: Output average of last N values
    Small N: less filtering
    Large N: more filtering, but less sharp output
12
12
Y
clk
X
digital filter

## Slide 45: Data Dominated RTL Design Example: FIR Filter
FIR filter
  “Finite Impulse Response”
  Simply a configurable weighted sum of past input values
  y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)
    Above known as “3 tap”
    Tens of taps more common
    Very general filter – User sets the constants (c0, c1, c2) to define specific filter
  RTL design
    Step 1: Create high-level state machine
      But there really is none! Data dominated indeed.
    Go straight to step 2
12
12
Y
clk
X
digital filter
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)

## Slide 46: Data Dominated RTL Design Example: FIR Filter
Step 2: Create datapath
  Begin by creating chain of xt registers to hold past values of X
12
12
Y
clk
X
digital filter
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)
180
180
181
180
181
240
Suppose sequence is: 180, 181, 240
a

## Slide 47: Data Dominated RTL Design Example: FIR Filter
Step 2: Create datapath (cont.)
  Instantiate registers for c0, c1, c2
  Instantiate multipliers to compute c*x values
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)
x
t0
x
t1
x
t2
x(
t
-2)
x(
t
-1)
x(t)
3-tap FIR filter
X
Y
clk
c1
c0
c2
*
*
*
a
12
12
Y
clk
X
digital filter

## Slide 48: Data Dominated RTL Design Example: FIR Filter
Step 2: Create datapath (cont.)
  Instantiate adders
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)
a
x
t0
x
t1
x
t2
x(
t
-2)
x(
t
-1)
x(t)
3-tap FIR filter
X
Y
clk
c0
c1
c2
*
*
*
+
+
12
12
Y
clk
X
digital filter

## Slide 49: Data Dominated RTL Design Example: FIR Filter
Step 2: Create datapath (cont.)
  Add circuitry to allow loading of particular c register
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)
a
12
12
Y
clk
X
digital filter
xt0
xt1
xt2
x(t-2)
x(t-1)
x(t)
3-tap FIR filter
X
Y
clk
c0
c1
c2
*
*
+
*
+
3
2
1
0
2x4
yreg
e
Ca1
CL
C
Ca0

## Slide 50: Data Dominated RTL Design Example: FIR Filter
Step 3 & 4: Connect to controller, Create FSM
  No controller needed
  Extreme data-dominated example
  (Example of an extreme control-dominated design – an FSM, with no datapath)
Comparing the FIR circuit to a software implementation
  Circuit
    Assume adder has 2-gate delay, multiplier has 20-gate delay
    Longest past goes through one multiplier and two adders
      20 + 2 + 2 = 24-gate delay
    100-tap filter, following design on previous slide, would have about a 34-gate delay: 1 multiplier and 7 adders on longest path
  Software
    100-tap filter: 100 multiplications, 100 additions. Say 2 instructions per multiplication, 2 per addition. Say 10-gate delay per instruction.
    (100*2 + 100*2)*10 = 4000 gate delays
  Circuit is more than 100 times faster (10,000% faster). Wow.
y(t) = c0*x(t) + c1*x(t-1) + c2*x(t-2)

## Slide 51: Determining Clock Frequency
Designers of digital circuits often want fastest performance
  Means want high clock frequency
Frequency limited by longest register-to-register delay
  Known as critical path
  If clock is any faster, incorrect data may be stored into register
  Longest path on right is 2 ns
    Ignoring wire delays, and register setup and hold times, for simplicity
5.4
a
+
b
c
2 ns
del
a
y
clk

## Slide 52: Critical Path
Example shows four paths
  a to c through +: 2 ns
  a to d through + and *: 7 ns
  b to d through + and *: 7 ns
  b to d through *: 5 ns
Longest path is thus 7 ns
Fastest frequency
  1 / 7 ns = 142 MHz
+
*
c
d
7 ns
7 ns
5 ns
delay
2 ns
delay
Max
(2,7,7,5)
= 7 ns
a
b
5 ns
7 ns
7 ns
2 ns

## Slide 53: Critical Path Considering Wire Delays
Real wires have delay too
  Must include in critical path
Example shows two paths
  Each is 0.5 + 2 + 0.5 = 3 ns
Trend
  1980s/1990s: Wire delays were tiny compared to logic delays
  But wire delays not shrinking as fast as logic delays
    Wire delays may even be greater than logic delays!
Must also consider register setup and hold times, also add to path
Then add some time to the computed path, just to be safe
  e.g., if path is 3 ns, say 4 ns instead
a
+
b
c
2 ns
3 ns
3 ns
0.5 ns
0.5 ns
0.5 ns
clk
3 ns

## Slide 54: A Circuit May Have Numerous Paths
Paths can exist
  In the datapath
  In the controller
  Between the controller and datapath
  May be hundreds or thousands of paths
Timing analysis tools that evaluate all possible paths automatically very helpful
Combinational logic
c
tot_lt_s
clk
n1
d
tot_ld
tot_lt_s
t
ot_clr
s0
s1
n0
State register
s
8
8
8
8
a
ld
clr
tot
Datapath
8-bit
<
8-bit
adder
(
c
)
(
b
)
(
a
)

## Slide 55: Behavioral Level Design: C to Gates
Earlier sum-of-absolute-differences example
  Started with high-level state machine
  C code is an even better starting point -- easier to understand
5.5
!go
S0
go
S1
sum = 0
i = 0
S3
sum=sum+abs(A[i]-B[i])
i=i+1
S4
sad_
r
eg = sum
S2
i<256
(i<256)’
a
i
n
t SAD (byte A[256], byte B[256]) // not quite C syntax
{
uint sum; short uint I;
sum = 0;
i = 0;
while (i < 256) {
sum = sum + abs(A[i] – B[i]);
i = i + 1;
}
return sum;
}
C code

## Slide 56: Behavioral-Level Design: Start with C (or Similar Language)
Replace first step of RTL design method by two steps
  Capture in C, then convert C to high-level state machine
  How convert from C to high-level state machine?
Step 1A: Capture in C
Step 1B: Convert to high-level state machine
a

## Slide 57: Converting from C to High-Level State Machine
Convert each C construct to equivalent states and transitions
Assignment statement
  Becomes one state with assignment
If-then statement
  Becomes state with condition check, transitioning to “then” statements if condition true, otherwise to ending state
    “then” statements would also be converted to states
target = expression;
target=
expression
(then stmts)
if (cond) {
// then stmts
}
!cond
cond
(end)
a
a

## Slide 58: Converting from C to High-Level State Machine
If-then-else
  Becomes state with condition check, transitioning to “then” statements if condition true, or to “else” statements if condition false
While loop statement
  Becomes state with condition check, transitioning to while loop’s statements if true, then transitioning back to condition check
if (cond) {
// then stmts
}
else {
// else stmts
}
!cond
cond
(end)
(then stmts)
(else stmts)
while (cond) {
// while stmts
}
!cond
cond
(while stmts)
(end)
a
a

## Slide 59: Simple Example of Converting from C to High-Level State Machine
Simple example: Computing the maximum of two numbers
  Convert if-then-else statement to states (b)
  Then convert assignment statements to states (c)
(end)
(c)
X>Y
!(X>Y)
(end)
(then stmts)
(else stmts)
(b)
X>Y
!(X>Y)
Max=X
Max=Y
(a)
Inputs: uint X, Y
Outputs: uint Max
if (X > Y) {
}
else {
}
Max = X;
Max = Y;
a
a

## Slide 60: Example: Converting Sum-of-Absolute-Differences C code to High-Level State Machine
Convert each construct to states
  Simplify when possible, e.g., merge states
From high-level state machine, follow RTL design method to create circuit
Thus, can convert C to gates using straightforward automatable process
  Not all C constructs can be efficiently converted
  Use C subset if intended for circuit
  Can use languages other than C, of course
sum = sum + abs(A[i] - B[i]);
(a)
Inputs: byte A[256, B[256]
bit go;
Output: int sad
main()
{
uint sum; short uint I;
while (1) {
sum = 0;
i = 0;
while (!go);
while (i < 256) {
i = i + 1;
}
sad = sum;
}
}
(d)
!go
go
sum=0
i=0
(g)
!go
go
sum=0
i=0
!(i<256)
i<256
sad =
sum
sum=sum
+ abs
i = i + 1
sum=0
i=0
(b)
!(!go)
!go
(c)
!go
go
(e)
!go
go
sum=0
i=0
while stmts
!(i<256)
i<256
sad =
sum
(f)
!go
go
sum=0
i=0
!(i<256)
i<256
sum=sum
+ abs
i = i + 1
a

## Slide 61: Memory Components
Register-transfer level design instantiates datapath components to create datapath, controlled by a controller
  A few more components are often used outside the controller and datapath
MxN memory
  M words, N bits wide each
Several varieties of memory, which we now introduce
5.6
N-bits
wide each
M
×
N
memo
r
y
M words

## Slide 62: Random Access Memory (RAM)
RAM – Readable and writable memory
  “Random access memory”
    Strange name – Created several decades ago to contrast with sequentially-accessed storage like tape drives
  Logically same as register file – Memory with address inputs, data inputs/outputs, and control
    RAM usually just one port; register file usually two or more
  RAM vs. register file
    RAM typically larger than roughly 512 or 1024 words
    RAM typically stores bits using a bit storage approach that is more efficient than a flip flop
    RAM typically implemented on a chip in a square rather than rectangular shape – keeps longest wires (hence delay) short
32
10
data
addr
r
w
en
1024
×
32
R
A
M
32
4
32
4
W_data
W_addr
W_en
R_data
R_addr
R_en
16
×
32
register file
Register file from Chpt. 4
RAM block symbol

## Slide 63: RAM Internal Structure
Similar internal structure as register file
  Decoder enables appropriate word based on address inputs
  rw controls whether cell is written or read
  Let’s see what’s inside each RAM cell
32
10
data
addr
r
w
en
1024x32
RAM
addr0
addr1
addr(A-1)
clk
en
r
w
addr
Let A = log2M
to all cells
wdata(N-1)
rdata(N-1)
wdata(N-2)
rdata(N-2)
wdata0
rdata0
bit storage
block
(aka “cell”)
w
o
r
d
word
RAM cell
word
enable
word
enable
r
w
data cell
data
a0
a1
d0
d1
d(M-1)
a(A-1)
e
AxM
decoder
enable

## Slide 64: Static RAM (SRAM)
“Static” RAM cell
  6 transistors (recall inverter is 2 transistors)
  Writing this cell
    word enable input comes from decoder
    When 0, value d loops around inverters
      That loop is where a bit stays stored
    When 1, the data bit value enters the loop
      data is the bit to be stored in this cell
      data’ enters on other side
      Example shows a “1” being written into cell
a
SRAM cell
data
data’
d’
d
cell
0
word
enable
1
1
1
0
0
32
10
data
addr
r
w
en
1024x32
RAM
SRAM cell
data
data’
d
word
enable
data
data’
d’
d
cell
0
word
enable
1
0
a
a

## Slide 65: Static RAM (SRAM)
“Static” RAM cell
  Reading this cell
    Somewhat trickier
    When rw set to read, the RAM logic sets both data and data’ to 1
    The stored bit d will pull either the left line or the right bit down slightly below 1
    “Sense amplifiers” detect which side is slightly pulled down
  The electrical description of SRAM is really beyond our scope – just general idea here, mainly to contrast with DRAM...
SRAM cell
32
10
data
addr
r
w
en
1024x32
RAM
data
data’
d
1
1
1
word
enable
To sense amplifiers
1
0
1
<1
a

## Slide 66: Dynamic RAM (DRAM)
“Dynamic” RAM cell
  1 transistor (rather than 6)
  Relies on large capacitor to store bit
    Write: Transistor conducts, data voltage level gets stored on top plate of capacitor
    Read: Just look at value of d
    Problem: Capacitor discharges over time
      Must “refresh” regularly, by reading d and then writing it right back
DRAM cell
32
10
data
addr
r
w
en
1024x32
RAM
word
enable
data
c
ell
(
a
)
(
b
)
data
enable
d
discharges
d
capacitor
slowly
discharging

## Slide 67: Comparing Memory Types
Register file
  Fastest
  But biggest size
SRAM
  Fast
  More compact than register file
DRAM
  Slowest
    And refreshing takes time
  But very compact
Use register file for small items, SRAM for large items, and DRAM for huge items
  Note: DRAM’s big capacitor requires a special chip design process, so DRAM is often a separate chip
MxN Memory
implemented as a:
register
file
SRAM
DRAM
Size comparison for same
number of bits (not to scale)

## Slide 68: Reading and Writing a RAM
Writing
  Put address on addr lines, data on data lines, set rw=1, en=1
Reading
  Set addr and en lines, but put nothing (Z) on data lines, set rw=0
  Data will appear on data lines
Don’t forget to obey setup and hold times
  In short – keep inputs stable before and after a clock edge
clk
addr
data
r
w
en
1
2
9
9
13
999
Z
500
500
3
1 means write
RAM[9]
now equals 500
RAM[13]
now equals 999
(
b
)
valid
valid
Z
500
access
time
setup
time
hold
time
setup
time
clk
addr
data
r
w

## Slide 69: RAM Example: Digital Sound Recorder
Behavior
  Record: Digitize sound, store as series of 4096 12-bit digital values in RAM
    We’ll use a 4096x16 RAM (12-bit wide RAM not common)
  Play back later
  Common behavior in telephone answering machine, toys, voice recorders
To record, processor should read a-to-d, store read values into successive RAM words
  To play, processor should read successive RAM words and enable d-to-a

## Slide 70: RAM Example: Digital Sound Recorder
RTL design of processor
  Create high-level state machine
  Begin with the record behavior
  Keep local register a
    Stores current address, ranges from 0 to 4095 (thus need 12 bits)
  Create state machine that counts from 0 to 4095 using a
    For each a
      Read analog-to-digital conv.
        ad_ld=1, ad_buf=1
      Write to RAM at address a
        Ra=a, Rrw=1, Ren=1
ad_ld=1
ad_buf=1
Ra=a
Rrw=1
Ren=1
S
a=0
a=a+1
a=4095
a<4095
T
U
Local register:
a (12 bits)
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rw
Ren
Ra
12
16
processor
ad_buf
4096x16
RAM
a
Record behavior

## Slide 71: RAM Example: Digital Sound Recorder
  Now create play behavior
  Use local register a again, create state machine that counts from 0 to 4095 again
    For each a
      Read RAM
      Write to digital-to-analog conv.
    Note: Must write d-to-a one cycle after reading RAM, when the read data is available on the data bus
  The record and play state machines would be parts of a larger state machine controlled by signals that determine when to record or play
a
da_ld=1
ad_buf=0
Ra=a
Rrw=0
Ren=1
V
a=0
a=a+1
a=4095
a<4095
W
X
Local register:
a (12 bits)
Play behavior
data bus
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rw
Ren
Ra
12
16
processor
ad_buf
4096x16
RAM

## Slide 72: Read-Only Memory – ROM
Memory that can only be read from, not written to
  Data lines are output only
  No need for rw input
Advantages over RAM
  Compact: May be smaller
  Nonvolatile: Saves bits even if power supply is turned off
  Speed: May be faster (especially than DRAM)
  Low power: Doesn’t need power supply to save bits, so can extend battery life
Choose ROM over RAM if stored data won’t change (or won’t change often)
  For example, a table of Celsius to Fahrenheit conversions in a digital thermometer
32
10
data
addr
r
w
en
1024
×
32
R
A
M
RAM block symbol
32
10
data
addr
en
1024x32
ROM
ROM block symbol

## Slide 73: Read-Only Memory – ROM
Internal logical structure similar to RAM, without the data input lines
32
10
data
addr
en
1024x32
ROM
ROM block symbol
ROM cell
addr0
addr1
addr(A-1)
clk
en
addr
Let A = log2M
a0
a1
d0
d1
d(M-1)
a(A-1)
e
AxM
decoder
word
enable
rdata(N-1)
rdata(N-2)
rdata0
bit storage
block
(aka “cell”)
w
o
r
d
word
enable
word
enable
data
data

## Slide 74: ROM Types
If a ROM can only be read, how are the stored bits stored in the first place?
  Storing bits in a ROM known as programming
  Several methods
Mask-programmed ROM
  Bits are hardwired as 0s or 1s during chip manufacturing
    2-bit word on right stores “10”
    word enable (from decoder) simply passes the hardwired value through transistor
  Notice how compact, and fast, this memory would be
cell
cell
word
enable
data line
data line
0
1

## Slide 75: ROM Types
Fuse-Based Programmable ROM
  Each cell has a fuse
  A special device, known as a programmer, blows certain fuses (using higher-than-normal voltage)
    Those cells will be read as 0s (involving some special electronics)
    Cells with unblown fuses will be read as 1s
    2-bit word on right stores “10”
  Also known as One-Time Programmable (OTP) ROM
cell
cell
word
enable
data line
data line
1
1
blown fuse
fuse
a

## Slide 76: ROM Types
Erasable Programmable ROM (EPROM)
  Uses “floating-gate transistor” in each cell
  Special programmer device uses higher-than-normal voltage to cause electrons to tunnel into the gate
    Electrons become trapped in the gate
    Only done for cells that should store 0
    Other cells (without electrons trapped in gate) will be 1
      2-bit word on right stores “10”
    Details beyond our scope – just general idea is necessary here
  To erase, shine ultraviolet light onto chip
    Gives trapped electrons energy to escape
    Requires chip package to have window
c
ell
c
ell
word
enable
data line
data line
e
Ð
e
Ð
a
ting
g
a
t
e t
r
t
or
trapped electrons
0
1
floating-gate
transistor

## Slide 77: ROM Types
Electronically-Erasable Programmable ROM (EEPROM)
  Similar to EPROM
    Uses floating-gate transistor, electronic programming to trap electrons in certain cells
  But erasing done electronically, not using UV light
  Erasing done one word at a time
Flash memory
  Like EEPROM, but all words (or large blocks of words) can be erased simultaneously
  Become common relatively recently (late 1990s)
Both types are in-system programmable
  Can be programmed with new stored bits while in the system in which the ROM operates
    Requires bi-directional data lines, and write control input
    Also need busy output to indicate that erasing is in progress – erasing takes some time
a
ting
g
a
t
e t
r
t
or
32
10
data
addr
en
write
busy
1024x32
EEPROM

## Slide 78: ROM Example: Talking Doll
Doll plays prerecorded message, trigger by vibration
  Message must be stored without power supply  Use a ROM, not a RAM, because ROM is nonvolatile
    And because message will never change, use a mask-programmed ROM or OTP ROM
  Processor should wait for vibration (v=1), then read words 0 to 4095 from the ROM, writing each to the d-to-a
4096x16 ROM
processor
d
a
Ra
16
Ren
da_ld
digital-to-
analog
converter
v
speaker
vibration
sensor
“Hello there!”
“Hello there!” audio divided into 4096 samples, stored
in ROM
“Hello there!”
a

## Slide 79: ROM Example: Talking Doll
High-level state machine
  Create state machine that waits for v=1, and then counts from 0 to 4095 using a local register a
  For each a, read ROM, write to digital-to-analog converter
d
a
4096x16 ROM
processor
Ra
16
Ren
da_ld
digital-to-
analog
converter
v
S
a=0
da_ld=1
a=a+1
a=4095
a<4095
T
U
R
a=a
R
en=1
Local register:
a (12 bits)
v
v’
a

## Slide 80: ROM Example: Digital Telephone Answering Machine Using a Flash Memory
Want to record the outgoing announcement
  When rec=1, record digitized sound in locations 0 to 4095
  When play=1, play those stored sounds to digital-to-analog converter
What type of memory?
  Should store without power supply – ROM, not RAM
  Should be in-system programmable – EEPROM or Flash, not EPROM, OTP ROM, or mask-programmed ROM
  Will always erase entire memory when reprogramming – Flash better than EEPROM
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rrw
Ren
er
bu
Ra
12
16
processor
ad_buf
busy
4096x16 Flash
rec
play
record
microphone
speaker
“We’re not home.”

## Slide 81: ROM Example: Digital Telephone Answering Machine Using a Flash Memory
High-level state machine
  Once rec=1, begin erasing flash by setting er=1
  Wait for flash to finish erasing by waiting for bu=0
  Execute loop that sets local register a from 0 to 4095, reading analog-to-digital converter and writing to flash for each a
d
a
r
w
en
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rrw
Ren
er
bu
Ra
12
16
processor
ad_buf
4096x16 Flash
rec
play
record
microphone
speaker
T
er=0
bu
bu’
er=1
r
ec
S
Local register: a (13 bits)
a=4096
a<4096
U
V
ad_ld=1
ad_buf=1
Ra=a
Rrw=1
Ren=1
a=a+1
a=0
a

## Slide 82: Blurring of Distinction Between ROM and RAM
We said that
  RAM is readable and writable
  ROM is read-only
But some ROMs act almost like RAMs
  EEPROM and Flash are in-system programmable
    Essentially means that writes are slow
      Also, number of writes may be limited (perhaps a few million times)
And, some RAMs act almost like ROMs
  Non-volatile RAMs: Can save their data without the power supply
    One type: Built-in battery, may work for up to 10 years
    Another type: Includes ROM backup for RAM – controller writes RAM contents to ROM before turning off
New memory technologies evolving that merge RAM and ROM benefits
  e.g., MRAM
Bottom line
  Lot of choices available to designer, must find best fit with design goals
EEPROM
ROM
Flash
NVRAM
RAM
a

## Slide 83: Queues
A queue is another component sometimes used during RTL design
Queue: A list written to at the back, from read from the front
  Like a list of waiting restaurant customers
Writing called a push, reading called a pop
Because first item written into a queue will be the first item read out, also called a FIFO (first-in-first-out)
5.7
front
back
write items
to the back
of the queue
read (and
remove) items
from front of
the queue

## Slide 84: Queues
Queue has addresses, and two pointers: rear and front
  Initially both point to 0
Push (write)
  Item written to address pointed to by rear
  rear incremented
Pop (read)
  Item read from address pointed to by front
  front incremented
If front or rear reaches 7, next (incremented) value should be 0 (for a queue with addresses 0 to 7)
r f
0
1
2
3
4
5
6
7
f
r
0
A
1
2
3
4
5
6
7
A
f
r
0
A
B
1
2
3
4
5
6
7
B
f
r
0
B
1
2
3
4
5
6
7
A
a
a
a

## Slide 85: Queues
Treat memory as a circle
  If front or rear reaches 7, next (incremented) value should be 0 rather than 8 (for a queue with addresses 0 to 7)
Two conditions of interest
  Full queue – no room for more items
    In 8-entry queue, means 8 items present
    No further pushes allowed until a pop occurs
    Causes front=rear
  Empty queue – no items
    No pops allowed until a push occurs
    Causes front=rear
  Both conditions have front=rear
    To detect whether front=rear means full or empty, need state machine that detects if previous operation was push or pop, sets full or empty output signal (respectively)
f
r
0
B
1
2
3
4
5
6
7
A
B
1
7
2
6
3
5
4
0
f
r
r
a

## Slide 86: Queue Implementation
Can use register file for item storage
Implement rear and front using up counters
  rear used as register file’s write address, front as read address
Simple controller would set control lines for pushes and pops, and also detect full and empty situations
  FSM for controller not shown

## Slide 87: Common Uses of a Queue
Computer keyboard
  Pushes pressed keys onto queue, meanwhile pops and sends to computer
Digital video recorder
  Pushes captured frames, meanwhile pops frames, compresses them, and stores them
Computer network routers
  Pushes incoming packets onto queue, meanwhile pops packets, processes destination information, and forwards each packet out over appropriate port

## Slide 88: Queue Usage Example
Example series of pushes and pops
  Note how rear and front pointers move
  Note that popping doesn’t really remove the data from the queue, but that data is no longer accessible
  Note how rear (and front) wraps around from address 7 to 0
Note: pushing a full queue is an error
  As is popping an empty queue

## Slide 89: Hierarchy – A Key Design Concept
Hierarchy
  An organization with a few items at the top, with each item decomposed into other items
  Common example: A country
    1 item at the top (the country)
    Country item decomposed into state/province items
    Each state/province item decomposed into city items
Hierarchy helps us manage complexity
  To go from transistors to gates, muxes, decoders, registers, ALUs, controllers, datapaths, memories, queues, etc.
  Imagine trying to comprehend a controller and datapath at the level of gates
5.8
P
r
o
vin
c
e 3
P
r
o
vin
c
e 2
P
r
o
vin
c
e 1
CityF
Country A
vin
vin
vin
P
r
o
c
P
r
o
c
e 2
P
r
o
c
e 1
Province 1
Province 2
Province 3
Province 1
Province 2
Province 3
Map showing all levels of hierarchy
Map showing just top two levels of hierarchy
CityG
CityE
CityD
CityA
CityB
CityC
Country A

## Slide 90: Hierarchy and Abstraction
Abstraction
  Hierarchy often involves not just grouping items into a new item, but also associating higher-level behavior with the new item, known as abstraction
    e.g., an 8-bit adder has an understandable high-level behavior – it adds two 8-bit binary numbers
  Frees designer from having to remember, or even from having to understand, the lower-level details
P
r
o
vin
c
e 3
P
r
o
vin
c
e 2
P
r
o
vin
c
e 1
vin
vin
vin
P
r
o
c
e 3
P
r
o
c
e 2
P
r
o
c
e 1
a7.. a0
b7.. b0
s7.. s0
c
o
ci
8-bit adder

## Slide 91: Hierarchy and Composing Larger Components from Smaller Versions
A common task is to compose smaller components into a larger one
  Gates: Suppose you have plenty of 3-input AND gates, but need a 9-input AND gate
    Can simple compose the 9-input gate from several 3-input gates
  Muxes: Suppose you have 4x1 and 2x1 muxes, but need an 8x1 mux
    s2 selects either top or bottom 4x1
    s1s0 select particular 4x1 input
    Implements 8x1 mux – 8 data inputs, 3 selects, one output
P
r
o
vin
c
e 3
P
r
o
vin
c
e 2
P
r
o
vin
c
e 1
vin
vin
vin
P
r
o
c
e 3
P
r
o
c
e 2
P
r
o
c
e 1
a

## Slide 92: Hierarchy and Composing Larger Components from Smaller Versions
Composing memory very common
Making memory words wider
  Easy – just place memories side-by-side until desired width obtained
  Share address/control lines, concatenate data lines
  Example: Compose 1024x8 ROMs into 1024x32 ROM
P
r
o
vin
c
e 3
P
r
o
vin
c
e 2
P
r
o
vin
c
e 1
vin
P
r
o
c
e 3
P
r
o
P
r
o
1024x32
ROM
1024x8
ROM
data
addr
en
data
8
8
32
8
8
10
10
en
en
addr
addr
data(31..0)
1024x8
ROM
addr
en
data
1024x8
ROM
addr
en
data
1024x8
ROM
addr
en
data

## Slide 93: Hierarchy and Composing Larger Components from Smaller Versions
Creating memory with more words
  Put memories on top of one another until the number of desired words is achieved
  Use decoder to select among the memories
    Can use highest order address input(s) as decoder input
    Although actually, any address line could be used
  Example: Compose 1024x8 memories into 2048x8 memory
P
r
o
vin
c
e 3
P
r
o
vin
c
e 2
P
r
o
vin
c
e 1
vin
vin
P
r
o
c
e 3
P
r
o
c
e 2
P
1024x8
ROM
addr
en
data
1024x8
ROM
addr
en
data
0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 0 0 1 0
0 1 1 1 1 1 1 1 1 1 0
0 1 1 1 1 1 1 1 1 1 1
1 0 0 0 0 0 0 0 0 0 0
1 0 0 0 0 0 0 0 0 0 1
1 0 0 0 0 0 0 0 0 1 0
1 1 1 1 1 1 1 1 1 1 0
1 1 1 1 1 1 1 1 1 1 1
a0
a10
a9
a8
a10 just chooses which memory to access
To create memory with more words and wider words, can first compose to enough words, then widen.
a
a
2048x8
ROM
data
8
11
11
en
addr
1024x8
ROM
addr
en
data
8
1024x8
ROM
addr
en
data
8
a9..a0
a10
d0
d1
en
addr
1x2
dcd
i0
e

## Slide 94: Chapter Summary
  Modern digital design involves creating processor-level components
  Four-step RTL method can be used
    1. High-level state machine 2. Create datapath 3. Connect datapath to controller 4. Derive controller FSM
  Several example
    Control dominated, data dominated, and mix
  Determining fastest clock frequency
    By finding critical path
  Behavioral-level design – C to gates
    By using method to convert C (subset) to high-level state machine
  Additional RTL components
    Memory: RAM, ROM
    Queues
  Hierarchy: A key concept used throughout Chapters 2-5